## Slide 1: 5G WIRELESS COMMUNICATION (UEC 719)
Course Instructor
Dr. Hem Dutt Joshi
Dr. Surbhi Sharma
Associate Professor,
TIET, Patiala

## Slide 2
5G WIRELESS COMMUNICATION (UEC 719)
Dr. Amit Mishra
Associate Professor,
TIET, Patiala
Dr. Surbhi Sharma
Associate Professor,
TIET, Patiala

## Slide 3
Lecture: 13
5G NR
Numerology and Resource Block

## Slide 4
Contents
OFDM SYSTEM MODEL
5G NR Numerologies,
Sub Carrier Spacing
Resource Block

## Slide 5: OFDM System
IFFT takes frequency-domain input data (complex numbers representing the modulated subcarriers) and converts it to the time-domain output data
(analog OFDM symbol waveform)
Thus, the IFFT block provides a simple way to modulate data onto N orthogonal subcarriers.

## Slide 6: Numerologies in 5G NR
5G NR supports QPSK, 16 QAM, 64 QAM and 256 QAM modulation
5G New Radio uses OFDM wave form
It uses variable sub carrier spacing
In 4G LTE, subcarrier spacing used is 15KHz
In 5G, possible sub carrier spacings are
  15KHz, 30KHz,
  60KHz, 120KHz
  240KHz

## Slide 7: Numerology and Sub Carrier Spacing
µ=1 (Numerology 1 )
SCS = 30 KHz
Sub Carrier Spacing = 2µ x 15 KHz
µ=2 (Numerology 2 )
SCS = 60 KHz
µ=3 (Numerology 3 )
SCS = 120 KHz
µ=4 (Numerology 4 )
SCS = 240 KHz

## Slide 8
Resource Block

## Slide 9: Resource Block and its Bandwidth
12 Consecutive Sub carriers constitute one Resource Block (RB)
Sub Carrier Spacing = 2µ x 15 KHz

## Slide 10: Recourse Block and its BW
BW of RG for various Numerologies
=SCSx12
µ=0 (Numerology 0 )
µ=1 (Numerology 1 )
µ=2 (Numerology 2)
µ=3 (Numerology 3 )
µ=4 (Numerology 4 )
RB = 12 contiguous Sub Carriers

## Slide 11: Numerology , Sub Carrier Spacing and Resource Block

## Slide 12: Example
= 135
For the following parameters: Channel BW=50 MHz, Numerology =0, and Guard Band = 692.5 KHz; Determine Transmission BW and No. of Sub-carriers.
Sub Carrier Spacing = 2µ x 15 KHz
2µ =1
µ = 0

## Slide 13: Example
Given Parameters:
Channel BW = 100 MHz
Numerology-2 (µ=2) --- SCS = 60KHz
Guard Band = 1370 KHz
Determine Transmission BW, No. of Sub-carriers and Resource Block , Bandwidth of RB
Transmission BW = 97.26 MHz (100 MHz- 2 * 11370 kHz)
No. of Sub-Carriers = 1621 (97.26 * 10^6 / 60 KHz)
No. of RBs = 1621/12 = 135
Band width of one RB = 12 * 60 = 720 KHz

## Slide 14: UE Channel Bandwidth
The UE channel bandwidth supports a single NR RF carrier
BS supports different UE channel bandwidths within the same BS spectrum.
BS supports Transmission of multiple carriers to the same UE (CA) or multiple carriers to different UEs within BS Channel BW
UE is configured with one or more BWP / carriers, each with its own UE channel BW
3GPP TS38.101-1

## Slide 15: UE Channel Bandwidth
3GPP TS38.101-1

## Slide 16: Maximum Transmission Bandwidth FR1
3GPP TS38.101-1
3GPP has specified Channel bandwidths for each NR band

## Slide 17: Maximum Transmission Bandwidth FR2
3GPP TS38.101-2

## Slide 18: Min and Max Channel BW

## Slide 19: Maximum Supported BW for each Numerology
50 MHz
SCS =15 KHz
100 MHz
SCS = 30 KHz
100 MHz
SCS = 60 KHz
200 MHz
SCS =60 KHz
400 MHz
SCS = 60 KHz
400 MHz
SCS = 240 KHz
FR1
FR2
SCS = 120 KHz
SCS = 240 KHz

## Slide 20: Usage example of numerologies, Spectrum Band and cell size

## Slide 21: Usage example of Frequency Band and SCS