## Slide 1: 5G WIRELESS COMMUNICATION (UEC 719)
1
Dr. Amit Mishra
Associate Professor,
TIET, Patiala
Dr. Surbhi Sharma
Associate Professor,
TIET, Patiala

## Slide 2
Lecture: 15
5G NR
Bandwidth Part (BWP)

## Slide 3
Contents
Bandwidth Part (BWP)

## Slide 4: Bandwidth part
A bandwidth part is a subset of contiguous common physical resource blocks (PRBs).
A UE can support less than the carrier BW
LTE
NR
20 MHz
All UEs support full carrier BW
Up to 400 MHz
Each bandwidth part (BWP) has its own numerology (i.e. cyclic prefix length and subcarrier spacing)
Only one BWP in the UL and one in the DL are active at a given time.
A UE can be configured with up to four BWPs in the uplink or four BWPs in the downlink.
A An additional four BWPs can be configured in a supplementary uplink.

## Slide 5: Bandwidth Part Use Cases
1) Supporting reduced UE bandwidth capability
Overall carrier
BWP
2) Supporting reduced UE energy consumption
Overall carrier
BWP # 1
BWP # 2
3) Supporting FDM of different numerologies
Overall carrier
BWP # 1
(num erology # 1)
BWP # 2
(num erology # 2)

## Slide 6: Bandwidth Part Use Cases
4) Supporting non-contiguous spectrum
Overall carrier
BWP # 1
BWP # 2
Something completely unknown
Overall carrier
BWP
Something new and not yet defined
?
5) Supporting forward compatibility

## Slide 7: Bandwidth parts
time
frequency
Switch of active bandwidth part
BWP #1 active
BWP #2 active
BWP #1 active

## Slide 8: CORSET in BWP