## Slide 1: Wireless and Mobile Communication (UEC 804)
Reference Text book
“Wireless communication_ principles and practices” (Second Edition )
Author: Theodore s Rapport
Publisher: Prentice Hall (2002)

## Slide 2
MODULE -IV

## Slide 3
Topics covered in this module till now
Propagation Basics
Topics to be covered in this video
Antenna Basics

## Slide 4
Antenna basics
dB unit can describe very big ratios with numbers of modest size. e.g
Tx power =100 W, Rx Power= 1W
    Tx power is 100 times of received power
    Difference is 20 dB
Tx power =100 W, Rx Power= 1mW
    Tx power is 100,000 times of received power
    Difference is 50 dB
Tx power =1000 W, Rx Power= 1mW
    Tx power is million times of received power
    Difference is 60 dB
What is Decibel(dB)
A logarithmic unit that is used to describe a ratio. Lets say, we have two values P1 and P2. the difference (ratio) between them can be expressed in dB and is computed as
10 log(P1/P2) dB
Transmit power P1= 100W, received power P2= 1W.
The difference is 10 log(100/1)= 20dB

## Slide 5
Antenna basics
dBm
For power differences, dBm is used to denote a power level with respect to 1mW as the reference power level.
Lets say Tx power of a system is 100 W . What is the Tx power in unit of dBm?
Solution:
Tx_power(dBm)=10 log(100W/1mW) = 10 log (100W/0.001W)= 10 log(100,0000)= 50dBm
dBW
For power differences, dBW is used to denote a power level with respect to 1W as the reference power level.
Lets say Tx power of a system is 100 W . What is the Tx power in unit of dBW?
Solution:
Tx_power(dBW)=10 log(100W/1W) = 10 log (100W/1W)= 10 log(100)= 20dBW

## Slide 6
Antenna basics
The free space received power is given by the friis free space equation
Pr(d)= PtGtGRλ2/(4π)2d2L
The gain of antenna G is related to its effective aperture by
G= 4π Ae/λ2
Where the effective aperture Ae is related to physical size of antenna
λ is related to carrier frequency by
λ=c/f = 2 π c/ ωc
Higher the frequency , higher the gain for same size antenna

## Slide 7
An isotropic radiator is an ideal antenna that radiates power with unit gain uniformly in all directions. It is used as the reference antenna in wireless systems
The effective isotropic radiated power(EIRP) is defined as
EIRP= PTGT
The effective radiated power(ERP) is the radiated power in comparison to the half wave dipole antenna
Since dipole antenna has a gain of 1.64(2.15dB)
ERP=EIRP-2.15(dB)
In practical antenna gains are given in units of dBi(dB gain with respect to an isotropic source
Antenna basics

## Slide 8
The path loss represents the signal attenuation as positive quantity and measured in dB
PL(dB)=10 log ( Pt/Pr)= -10 log( GtGRλ2/(4π)2d2)
When the antenna gains are excluded
PL(dB)=10 log ( Pt/Pr)= -10 log( λ2/(4π)2d2)
The Friis free space model is valid only in the far field or Fraunhofer region.
The Fraunhofer distance is defined as df=2D2/λ, Where D is the largest physical linear dimensions of antenna and additionally we must have df>> D and df>> λ
The Friis free space equation does not hold for d=0 Hence , we use a close-in power reference at distance d0 The reference distance is chosen such that do>df. Thus
Pr(d)=Pr(d0)log(do/d)2
Sometimes we define the received power with reference to 1 milli-watts as
Pr(d)=10log (Pr(d0)/0.001W)+20 log(d0/d) [in dBm]
Antenna basics

## Slide 9
Example(1)
Q. What will be the far field distance for a base station antenna with
  Largest antenna dimensions =0.5 m
  Frequency of operation f1=900 MHz
  Frequency of operation f2=1800MHz
Solution :
For 900 MHz
λ= (3*108/900 * 106)=0.33 m,
df=2D2/ λ=2(0.5)2 / (0.33)= 1.5 m
For 1800 MHz
λ= (3*108/1800 * 106)=0.17 m
df=2D2/ λ=2(0.5)2 / (0.17) =3 m

## Slide 10
Example(2)
For BS , let Pt= 10W, fc=900 MHz, Gt=2, Gr=1, The Mobile Station is at a distance of 5 KM. What is the received power in dBm?
Solution

## Slide 11
Example(3)
For a GSM BS , let Pt= 500 mW, fc=900 MHz, Gt=2, Gr=1, The Mobile Station is at a distance of 10 KM, What is the received power in dBm?
Solution

## Slide 12
Example(4)
If a transmitter produces 50 W of power, express the transmit power in units of (a) dBm, and (b) dBW. If 50 W is applied to a unity gain antenna with a 900 MHz carrier frequency, find the received power in dBm at a free space distance of 100m from the antenna. Also find is Pr at 10 km ? Assume unity gain for the receiver antenna
Solution
Given: Transmitter power, Pt = 50 W
Carrier frequency, fc = 900 MHz
Transmitter power in dBm
Pt(dBm) = 101og [Pt(mW)/(1 mW)]= 101og [50 x 103] = 47.0 dBm.
Transmitter power, in dBW
Pt(dBW) = 101og[Pt(W)/(1 W)] = 101og[50] = 17.0 dBW.

## Slide 13
Mechanisms that affect the radio propagation
The received power at 100m can be determined
Given d0 = 100m and d = 10 km, The received power at 10 km can be expressed in terms of dBm as