## Slide 1: Wireless and Mobile Communication (UEC 804)
Reference Text book
“Wireless communication_ principles and practices” (Second Edition )
Author: Theodore s Rapport
Publisher: Prentice Hall (2002)

## Slide 2
MODULE -IV

## Slide 3
Topics covered till now in this module
Propagation Basics
Topics to be covered in this video
Antenna Basics
Two Ray Model
Reflection
Diffraction
Outdoor propagation model
Scattering

## Slide 4
Outdoor propagation Models
Outdoor radio transmission takes place over an irregular terrain.
The terrain profile must be taken into consideration for estimating the path loss e.g. trees buildings and hills must be taken into consideration
Some common models used are
  Longley Rice Model
  Okumura Model
  Hata model

## Slide 5
Longley Rice Model
Longley Rice Model is applicable to point to point communication.
It covers 40MHz to 300 GHz
It can be used in wide range of terrain
Path geometry of terrain and the refractivity of troposphere is used for transmission path loss calculations
Geometrical optics is also used along with the two ray model for the calculation of signal strength.
  Two modes
    Point to point mode prediction
    Area mode prediction

## Slide 6
Longley Rice Model
Longley Rice Model is normally available as a computer program which takes inputs as transmission frequency
Path length
Polarization
Antenna heights
Surface reflectivity
Ground conductivity and dialectic constant
Climate factors
A problem with Longley rice is that It doesn't take into account the buildings and multipath.