## Slide 1: Wireless and Mobile Communication (UEC 804)
Reference Text book
“Wireless communication_ principles and practices” (Second Edition )
Author: Theodore s Rapport
Publisher: Prentice Hall (2002)

## Slide 2
MODULE -V
Mobile Radio Propagation: Small-Scale Fading and Multipath

## Slide 3
Topics covered till now in this module
Introduction to fading
Topic to be covered in this video
Factors influencing the fading

## Slide 4
Types of Small-Scale Fading
Fading can be caused by two independent MRC propagation mechanisms:
  1) time dispersion → multipath delay (Bc , Ts )
  2) frequency dispersion → Doppler spread (BD , Tc)
    Important digital Tx signal parameters → symbol period & signal BW

## Slide 5
Fading
A pulse can be more than two levels, however, so each period would be called a "symbol period".
  We send 0 (say +1 Volt) or 1 (say -1 Volt) → one bit per “symbol”
  Or we could send 10 (+3 Volts) or 00 (+1 Volt) or 01 (-1 Volt) or 11 (-3 Volts) → two bits per “symbol”

## Slide 6
illustrates types of small-scale fading

## Slide 7
Fading due to Multipath Delay(Flat fading)
  A）Flat Fading → Bs << Bc or Ts >>
    signal fits easily within the bandwidth of the channel
    channel BW >> signal BW
    most commonly occurring type of fading

## Slide 8
Flat fading
spectral properties of Tx signal are preserved
  signal is called a narrowband channel, since the bandwidth of the signal is narrow with respect to the channel bandwidth
  signal is not distorted
What does Ts >> mean??
  all multipath signals arrive at mobile Rx during 1 symbol period
  Little intersymbol interference occurs (no multipath components arrive late to interfere with the next symbol)

## Slide 9
Fading due to Multipath Delay

## Slide 10
Fading due to Multipath Delay
flat fading is generally considered desirable
  Even though fading in amplitude occurs, the signal is not distorted
  Forward link → can increase mobile Rx gain (automatic gain control)
  Reverse link → can increase mobile Tx power (power control)
  Can use diversity techniques (described in a later lecture)

## Slide 11
Frequency Selective Fading
B) Frequency Selective Fading → Bs > Bc or Ts <
  Bs > Bc → certain frequency components of the signal are attenuated much more than others

## Slide 12
Frequency Selective Fading

## Slide 13
Frequency Selective Fading
Ts < στ → delayed versions of Tx signal arrive during different symbol periods
    e.g. receiving an LOS → “1” & multipath “0” (from prior symbol!)
    This results in intersymbol interference (ISI)
    Undesirable
it is very difficult to predict mobile Rx performance with frequency selective channels

## Slide 14
Frequency Selective Fading
But for high bandwidth applications, channels with likely be frequency selective
    a new modulation approach has been developed to combat this called OFDM
One aspect of OFDM is that it separates a wideband signal into many smaller narrowband signals
    Then adaptively adjusts the power of each narrowband signal to fit the characteristics of the channel at that frequency.
    Results in much improvement over other wideband transmission approaches (like CDMA).

## Slide 15
Frequency Selective Fading
  OFDM is used in the new 802.11g 54 Mbps standard for WLAN’s in the 2.4 GHz band.
  Previously it was thought 54 Mbps could only be obtained at 5.8 GHz using CDMA, but 5.8 GHz signals attenuate much more quickly.
  Signals are split using signal → FFT, break into pieces in the frequency domain, use inverse FFT to create individual signals from each piece, then transmit.

## Slide 16
Fading due to Doppler Spread(Fast Fading)
  Caused by motion of Tx and Rx and reflection sources.
  A) Fast Fading → Bs < BD or Ts > Tc
    Bs < BD
      Doppler shifts significantly alter spectral BW of TX signal
    signal “spreading” Ts > Tc
      MRC changes within 1 symbol period
      rapid amplitude fluctuations
    uncommon in most digital communication systems

## Slide 17
Slow fading
Slow Fading → Ts << Tc or Bs >> BD
  MRC constant over many symbol periods
  slow amplitude fluctuations
  for v = 60 mph @ fc = 2 GHz → BD = 178 Hz
  ∴ Bs ≈ 2 kHz >> BD and Bs almost always >> BD for most applications
** NOTE: Typically use a factor of 10 to designate “>>” **

## Slide 18
Fading due to Doppler Spread

## Slide 19: Fading Signal Distributions
Rayleigh probability distribution function →
  Used for flat fading signals.
  Formed from the sum of two Gaussian noise signals.
  σ : RMS value of Rx signal before detection (demodulation)
  common model for Rx signal variation
    urban areas → heavy clutter → no LOS path
  probability that signal does not exceeds predefined threshold level R

## Slide 20
Rayleigh PDF

## Slide 21
  rmean : The mean value of Rayleigh distribution
  σr2 : The variance of Rayleigh distribution; ac power of signal envelope
    σ : RMS value of Rx signal before detection (demodulation)
Rayleigh distribution

## Slide 22
Rayleigh distribution

## Slide 23
  one dominant signal component along with weaker multipath signals
  dominant signal → LOS path
    suburban or rural areas with light clutter
  becomes a Rayleigh distribution as the dominant component weakens
Ricean distribution

## Slide 24
Ricean distribution