## Slide 1: 5G WIRELESS COMMUNICATION (UEC 719)
Course Instructor
Dr. Hem Dutt Joshi
Dr. Surbhi Sharma
Associate Professor,
TIET, Patiala

## Slide 2
Lecture: 16
5G NR
Frame Structure

## Slide 3
Contents
Frame Structure in Time Domain

## Slide 4: Frame Structure in Time domain
Frame
Sub Frame
Slot
Symbols

## Slide 5: Radio Frame
Symbol duration : Varies according to sub
carrier spacing used.
OFDM Symbols per slot = 14
Slot Duration : Varies according to
sub carrier spacing used.
Subframe duration = 1msec
Frame duration = 10msec

## Slide 6: Slot Length

## Slide 7: No. of Slots in frame/Sub Frame
SCS
Slot per Sub Frame (1ms)
Symbols per Sub Frame (1ms)
15KHz
30KHz
60KHz
120KHz
240KHz
Slot per Frame (10ms)
Symbol per Frame(10ms)

## Slide 8: 15 KHz sub carrier
Frame duration = 10 mSec
Sub frame duration = 1 msec
Slots per sub frame = 1 slot
Slot duration = 1msec
Symbols per slot = 14 symbols
Symbols per SF = 14
Symbol per F = 140

## Slide 9: 30 KHz sub carrier
Frame duration = 10 mSec
Sub frame duration = 1 msec
Slots/ subframe = 2 slot
Slot duration = 0.5 msec
Symbols/ slot = 14 symbols
Symbols per SF = 28
Symbols per F = 280

## Slide 10: 60 KHz sub carrier
Frame duration = 10 mSec
Sub frame duration = 1 msec
Slots / SF = 4 slot
Slot duration = 0.25 msec
Symbols/ slot = 12/14 symbols
Symbols per SF = 56
Symbol per F = 560

## Slide 11: 120 KHz sub carrier
Slots/SF = 8 slot
Slot duration = 0.125 msec
Symbols /slot = 14 symbols
Symbols per SF =112
Symbol per F =1120

## Slide 12: 240 KHz sub carrier
Slots / subframe = 16 slot
Slot duration = 0.0625 msec
Symbols / slot = 14 symbols
Symbols per SF = 288
Symbol per F =2880

## Slide 13: Frame Structure

## Slide 14: Sub carrier spacing and slot duration

## Slide 15: Symbol in a slot