## Slide 1: 5G WIRELESS COMMUNICATION (UEC 719)
Course Instructor
Dr. Hem Dutt Joshi
Dr. Surbhi Sharma
Associate Professor,
TIET, Patiala

## Slide 2
Lecture
5G Core Network Architecture
Standalone and Non-Standalone Mode

## Slide 3
Non-Standalone Mode (NSA) in 5G
  NSA mode is an initial deployment option for 5G that builds upon existing 4G LTE infrastructure.
  In NSA mode, the 5G network relies on the 4G core network for essential functions such as authentication, mobility management, and session management.
  The 5G radio access network (RAN) is added to the existing 4G network, which can allow for faster data speeds and lower latency compared to 4G.
Standalone Mode vs. Non-Standalone Mode in 5G
Standalone Mode (SA) in 5G
  SA mode is a fully independent 5G deployment.
  In SA mode, both the 5G RAN and the 5G core network are deployed, enabling the full capabilities of 5G technology.
  SA mode allows for advanced features like network slicing, which enables the creation of virtual networks tailored to specific use cases.
  It also provides improved support for Internet of Things (IoT) devices and applications. SA mode is considered the ultimate goal for 5G deployment, as it unlocks the full transformative potential of 5G technology.

## Slide 4
Core Network:
In NSA mode, the 5G network relies on the existing 4G core network, while SA mode deploys a dedicated 5G core network. This distinction allows SA mode to fully leverage the advanced functionalities and capabilities of 5G.
Features and Capabilities:
NSA mode can provide faster data speeds and lower latency compared to 4G, but it may not fully realize the potential of ultra-reliable low latency communication (URLLC) and massive machine-type communication (mMTC) that 5G promises. SA mode, on the other hand, enables the full suite of 5G features, including network slicing, improved IoT support, and enhanced reliability.
Key Difference between Standalone and Non-Standalone

## Slide 5
Short-Term vs. Long-Term Solutions:
While NSA mode offers a quicker and more cost-effective way to introduce 5G, SA mode is considered the long-term solution.
SA mode provides a foundation for future innovations and use cases, ensuring that the network is ready to support emerging technologies and applications.
As 5G continues to evolve, SA mode will become the standard for 5G deployments.
The advanced capabilities of SA mode will help enable a wide range of transformative applications, including autonomous vehicles, smart cities, remote surgery, and immersive virtual reality experiences.
Key Difference between Standalone and Non-Standalone