## Slide 1: 5G WIRELESS COMMUNICATION (UEC 719)
Dr. Amit Mishra
Associate Professor,
TIET, Patiala
Dr. Surbhi Sharma
Associate Professor,
TIET, Patiala

## Slide 7
Quiz-1
Evolution of wireless Communication Standards from 2G to 5G

## Slide 8
1. What does 1G stand for? A. First Grade B. First Generation C. Fast Generation D. Frequency Generation
2. Which technology was used in 1G? A. GSM B. CDMA C. Analog D. LTE
3. The primary use of 1G was: A. Video calling B. Voice communication C. SMS and MMS D. Internet browsing
4. What is one major drawback of 1G? A. Low cost B. High data rate C. Poor voice quality and security D. Long battery life
5. In which decade was 1G introduced? A. 1960s B. 1970s C. 1980s D. 1990s
6. Which technology was introduced in 2G? A. LTE B. Analog C. GSM D. CDMA2000
7. 2G networks use which kind of signals? A. Digital B. Analog C. Optical D. Infrared
8. What service was introduced with 2G? A. Voice over IP B. SMS C. Video streaming D. App store

## Slide 9
9. What is the typical data rate of 2G? A. Up to 10 Kbps B. Up to 64 Kbps C. 1 Mbps D. 100 Mbps
10. Which of the following is a 2G technology? A. UMTS B. EDGE C. HSPA D. OFDMA
11. Which technology is widely associated with 3G? A. GSM B. LTE C. WCDMA D. OFDM
12. What major service became common with 3G? A. Voice-only calling B. SMS C. High-speed internet access D. Analog video
13, What is the typical data speed of 3G? A. 144 Kbps B. 384 Kbps to 2 Mbps C. 10 Mbps D. 100 Mbps
14. Which of the following is NOT a 3G technology? A. UMTS B. CDMA2000 C. EDGE D. HSPA
15. Which year did 3G begin widespread adoption? A. 1991 B. 1999 C. 2005 D. 2010
16. Which technology is the backbone of 4G? A. LTE B. GSM C. WCDMA D. EDGE

## Slide 10
17. What is the maximum theoretical speed of 4G LTE? A. 10 Mbps B. 100 Mbps C. 1 Gbps D. 10 Gbps
18. Which of the following is a key feature of 4G? A. Analog transmission B. IP-based communication C. Circuit switching D. No internet access
19. Which application became popular due to 4G? A. Fax B. Streaming HD videos C. Paging D. Morse code
20. What does LTE stand for? A. Light Transmission Efficiency B. Long-Term Evolution C. Local Transmission Exchange D. Line Termination Equipment
18. What is a key technology enabling 5G? A. GSM B. Circuit switching C. Massive MIMO D. CDMA
19. Which of the following is the highest theoretical speed of 5G? A. 1 Gbps B. 5 Gbps C. 10 Gbps D. 100 Mbps
20. What is the average latency expected in 5G? A. 100 ms B. 50 ms C. 10 ms D. 1 ms
21. Which frequency band is used in 5G mmWave? A. Below 1 GHz B. 1–2 GHz C. 3–6 GHz D. Above 24 GHz

## Slide 11
22. Which application is highly supported by 5G? A. Morse code B. HD radio C. Augmented Reality D. Voice-only calling
23. Which generation first introduced internet browsing on mobile phones? A. 1G B. 2G C. 3G D. 4G
24. Which of these is a use case for 5G? A. Slow SMS B. Self-driving cars C. Rotary phones D. Voice paging
25. What challenge does mmWave face in 5G? A. High penetration B. Low cost C. Short range and blockage D. Compatibility with 1G
26. What is a major goal of 5G compared to previous generations? A. Voice clarity B. Fax services C. Low latency and IoT integration D. Analog broadcasting
27. Which mobile generation introduced packet-switching as a key feature? A. 1G B. 2G C. 3G D. 5G
28. Which generation started using digital signal transmission? A. 1G B. 2G C. 3G D. 4G

## Slide 12
29. Which generation relies completely on IP-based communication? A. 2G B. 3G C. 4G D. 1G
30. Which generation has the highest spectrum efficiency? A. 2G B. 3G C. 4G D. 5G

## Slide 13
Quiz-1: Answers

## Slide 14
1. What does 1G stand for? A. First Grade B. First Generation C. Fast Generation D. Frequency Generation
2. Which technology was used in 1G? A. GSM B. CDMA C. Analog D. LTE
3. The primary use of 1G was: A. Video calling B. Voice communication C. SMS and MMS D. Internet browsing
4. What is one major drawback of 1G? A. Low cost B. High data rate C. Poor voice quality and security D. Long battery life
5. In which decade was 1G introduced? A. 1960s B. 1970s C. 1980s D. 1990s
6. Which technology was introduced in 2G? A. LTE B. Analog C. GSM D. CDMA2000
7. 2G networks use which kind of signals? A. Digital B. Analog C. Optical D. Infrared
8. What service was introduced with 2G? A. Voice over IP B. SMS C. Video streaming D. App store

## Slide 15
9. What is the typical data rate of 2G? A. Up to 10 Kbps B. Up to 64 Kbps C. 1 Mbps D. 100 Mbps
10. Which of the following is a 2G technology? A. UMTS B. EDGE C. HSPA D. OFDMA
11. Which technology is widely associated with 3G? A. GSM B. LTE C. WCDMA D. OFDM
12. What major service became common with 3G? A. Voice-only calling B. SMS C. High-speed internet access D. Analog video
13, What is the typical data speed of 3G? A. 144 Kbps B. 384 Kbps to 2 Mbps C. 10 Mbps D. 100 Mbps
14. Which of the following is NOT a 3G technology? A. UMTS B. CDMA2000 C. EDGE D. HSPA
15. Which year did 3G begin widespread adoption? A. 1991 B. 1999 C. 2005 D. 2010
16. Which technology is the backbone of 4G? A. LTE B. GSM C. WCDMA D. EDGE

## Slide 16
17. What is the maximum theoretical speed of 4G LTE? A. 10 Mbps B. 100 Mbps C. 1 Gbps D. 10 Gbps
18. Which of the following is a key feature of 4G? A. Analog transmission B. IP-based communication C. Circuit switching D. No internet access
19. Which application became popular due to 4G? A. Fax B. Streaming HD videos C. Paging D. Morse code
20. What does LTE stand for? A. Light Transmission Efficiency B. Long-Term Evolution C. Local Transmission Exchange D. Line Termination Equipment
18. What is a key technology enabling 5G? A. GSM B. Circuit switching C. Massive MIMO D. CDMA
19. Which of the following is the highest theoretical speed of 5G? A. 1 Gbps B. 5 Gbps C. 10 Gbps D. 100 Mbps
20. What is the average latency expected in 5G? A. 100 ms B. 50 ms C. 10 ms D. 1 ms
21. Which frequency band is used in 5G mmWave? A. Below 1 GHz B. 1–2 GHz C. 3–6 GHz D. Above 24 GHz

## Slide 17
22. Which application is highly supported by 5G? A. Morse code B. HD radio C. Augmented Reality D. Voice-only calling
23. Which generation first introduced internet browsing on mobile phones? A. 1G B. 2G C. 3G D. 4G
24. Which of these is a use case for 5G? A. Slow SMS B. Self-driving cars C. Rotary phones D. Voice paging
25. What challenge does mmWave face in 5G? A. High penetration B. Low cost C. Short range and blockage D. Compatibility with 1G
26. What is a major goal of 5G compared to previous generations? A. Voice clarity B. Fax services C. Low latency and IoT integration D. Analog broadcasting
27. Which mobile generation introduced packet-switching as a key feature? A. 1G B. 2G C. 3G D. 5G
28. Which generation started using digital signal transmission? A. 1G B. 2G C. 3G D. 4G

## Slide 18
29. Which generation relies completely on IP-based communication? A. 2G B. 3G C. 4G D. 1G
30. Which generation has the highest spectrum efficiency? A. 2G B. 3G C. 4G D. 5G

## Slide 19
Lecture: 1 to 3
Evolution of Mobile Technologies
1G to 6G

## Slide 20
Contents
Historical Milestones of Wireless Communication
Classification of mobile communication systems
Zero Generation Telephony
First Generation Mobile Systems
Second Generation Mobile Communication System (2G)
Third Generation (3G) Communication Systems
Fourth Generation (4G) Communication Systems
Fifth Generation (5G) Communication Systems
Beyond 5G

## Slide 21: Guglielmo Marconi
Historical Milestones of Wireless Communication

## Slide 22: Guglielmo Marconi
The first practical use of mobile-radio communication was demonstrated in 1897 by M G Marconi,
He successfully established radio transmission between a land-based station and a tugboat, over an 18 mi path.
Established a communication set up over 3 Km in 1896 using Morse code
Historical Milestones

## Slide 23
The Shannon capacity theorem defines the maximum amount of information, or data capacity, which can be sent over any channel or medium (wireless, coax, twister pair, fiber etc.)
Historical Milestones
In information theory, Shannon's source coding theorem (or noiseless coding theorem) establishes the statistical limits to possible data compression for data whose source is an independent identically-distributed (IID) random variable
Claude Shannon

## Slide 28: In 1965, Gordon Moore poised that roughly every two years the number of transistors on microchips will be double. Commonly referred to as Moore’s Law, this phenomenon suggests that computational progress will become significantly faster, smaller, and more efficient over time.
Historical Milestones
Gordon Moore

## Slide 29
Ancient Systems: Smoke Signals, Carrier Pigeons, …
Radio invented in the 1880s by Marconi
Many sophisticated military radio systems were developed during and after WW2
Cellular has enjoyed exponential growth since 1988, with many billion users worldwide today
  Ignited the wireless revolution
  Voice, data, and multimedia becoming ubiquitous
  Use in third world countries growing rapidly
Wireless History

## Slide 30: Classification of mobile communication systems
  Different mobile communication systems always exists in the different parts of the world.
  So collectively we are classifying all different system on the basis of generation wise development.
  They are called 0G, 1G, 2G, 3G, 4G, and 5G
  Simply, the "G" stands for "GENERATION".

## Slide 31: Classification of Mobile Communication Systems [T. S. Rappaport (2002)]
 | 1G | 2G | 3G | 4G
Carrier | Analog | Digital | Digital | Digital
Switching | Circuit | Circuit | Packet and Circuit | Packet
Services | Voice Only | Voice + Basic Data application | Voice + Advance Data (Multimedia) | Voice + Advance Multimedia
Capacity | Low | High | Very High | Un limited
Speed | - | Low Data Rate (up to 100 Kbps) | High Data Rate (up to 2 Mbps) | Very High Data Rate (> 100 Mbps)
Frequency Band | 800-900 MHz | 800-900 MHz | 1.8-2.5GHz | 2-8 GHz
Multiple Access | FDMA | TDMA and CDMA | Wideband Code Division Multiple Access (WCDMA), MC-CDMA, OFDM | Multi-Carrier Code Division Multiple Access. (MC-CDMA), OFDM
Notes: Different Mobile communication systems developed in the different parts of the world simultaneously.
Collectively, they can be classified on the basis of generation wise development.
They are called 0G, 1G, 2G, 3G and 4G.

## Slide 32: 1G to 5G Evolution
Mobile Technology is Continuously evolving
Every 10 Year next generation of mobile technology evolves
Every Next generation has brought over 10X increase in Capability
AMPS: Advanced Mobile Phone System
NMT: Nordic Mobile Telephone
TACS: Total Access Communication System
GSM: Global System for Mobile communication
HSPA: High Speed Packet Access
EVDO: Evolution-Data Optimized

## Slide 33: Early Mobile Telephony : 1940
0G- Zero Generation ( Mobile Radio Telephone)

## Slide 34: 0G- Zero Generation ( Mobile radio telephone)
Mobile radio telephone systems preceded modern cellular mobile telephony technology.
Since they were the predecessors of the first generation of cellular telephones, these systems are sometimes retroactively referred to as 0G (zero generation) systems.
Technologies used in 0G systems included the
  PTT (Push to Talk or manual).
  MTS (Mobile Telephone System) in 1946.
  IMTS (Improved Mobile Telephone Service) in 1966.
  AMTS (Advanced Mobile Telephone System) systems.
The primary users were loggers, construction foremen, realtors, and celebrities.

## Slide 35: 0G: Bell Lab Mobile Phone Service
Phone in Car
The 80-pound radios placed in the car
Call carried Partly on Radio and partly on PSTN
Operator Assisted
The system was demonstrated on June 17, 1946
PSTN: Public Switched Telephone Network

## Slide 36
https://www.youtube.com/watch?v=xDy2tHCPdk8
Small video by Bell labs on Early Mobile Telephony

## Slide 37: 1G- First Generation
These are the analog cellphone standards
Introduced in the 1980s and continued until being replaced by 2G digital cellphones.
Multiple Access Techniques -- FDMA.
Provide only voice and other telephone services.
Standards used in 1G
NMT (Nordic Mobile Telephone)
AMPS (Advanced Mobile Phone System)
TACS (Total Access Communications System)
C-450

## Slide 38: 1G Radio Characteristics
800 MHz and 900 MHz
Frequency
FDMA
Access technique
30 KHz
Channels Bandwidth
Frequency Modulation (FM)
Modulation
Analog voice
Service
Image Source : Qualcomm

## Slide 39: 1G Network and features
Foundation of Mobile
Analog Voice Poor voice quality Large phone size Poor battery life Limited capacity Poor reliability
Image Credit : Qualcomm
PSTN: Public Switched Telephone Network

## Slide 40
2G- Second Generation

## Slide 41
The technologies which are using by most’s of the today’s ubiquitous cellular networks are come under the 2G cellular standards.
These are the Digital cellphone standards.
Multiple Access Techniques -- TDMA and CDMA
Provide voice and data services.
Data speeds of up to 64 kbps
Enabled services such as SMS and MMS (Multimedia Message)
Provided better quality voice calls
2G- Second Generation

## Slide 42
2G standards based on TDMA
Global System for Mobile (GSM).
deployed widely in Europe, Asia, Australia, South America, and some parts of the US.
Interim standard 136 (IS-136).
widely used in North America, South America, and Australia.
Pacific Digital Cellular (PDC).
Japanese TDMA standard that is similar to IS-136.
2G standards based on CDMA
Interim standard 95 (IS-95)
It is also known as cdmaOne.
widely deployed by carriers in North America, as well as in Korea, Japan, China, South America, and Australia.

## Slide 43: Evolution to 2G
Image Credit : Qualcomm

## Slide 44: Evolution to 2G
Frequency re-use in 2G
Image Credit : Qualcomm

## Slide 45
Multiple Access Techniques

## Slide 46
Time division multiple Access Techniques
Frequency division multiple Access Techniques

## Slide 47
Code division multiple Access Techniques

## Slide 48
Transmitted signal
Received signal

## Slide 49
Code selection?

## Slide 50
Bandwidth calculation

## Slide 51
Band width in CDMA

## Slide 52
Method to generate a PN sequence for CDMA?
Linear feedback shift register (LFSR)

## Slide 53: 2G Network and features
Digital Voice
Increased System Capacity Mobility
SMS
Limited Data with GPRS/EDGE
GPRS (2.5G) up to 40kbps , evolved up to 171 kbps
EDGE (2.75G) up to 384kbps
SMSC
SGSN
GGSN
PDN
SIM: Subscriber Identity Module
BSS:Base Station Subsystem
BSC: Base Station Controller
MSC: Mobile Switching Center
BTS: Base Transceiver Station
VLR: Visitor Location Register
AuC: Authentication Center
HLR: Home Location Register
PDN : Public (Packet) Data Network
PSTN: Public Switched Telephone Network
GMSC: Gateway Mobile Switching Center
SMSC: Short Message Service Center
SGSN :Serving GPRS Support Node
GGSN: Gateway GPRS Support Node
GPRS: General Packet Radio Service
EDGE: (Enhanced Data rates for GSM Evolution)

## Slide 54
Architecture of the GSM system
GSM is a PLMN (Public Land Mobile Network)
Components
  MS (mobile station)
  BS (base station)
  BSC (Base switching center)
  MSC (mobile switching center)
  LR(Location Registers)
Subsystems
  RSS (radio subsystem): covers all radio aspects
  NSS (network and switching subsystem): call forwarding, handover, switching
  OSS (operation subsystem): management of the network

## Slide 55
NSS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
RSS
radio cell
MS MS
radio cell
MS
AUC
OSS
signaling ISDN, PSTN
PDN
O
GSM: elements and interfaces
Abis interface
This is a BSS internal interface linking the BSC and a BTS.
The Abis interface allows control of the radio equipment and radio frequency allocation in the BTS.
A interface
The A interface is used to provide communication between the BSS and the MSC.
The interface carries information to enable the channels, timeslots and the like to be allocated to the mobile equipments being serviced by the BSSs.
BSS: Base Station Subsystem
BSC: Base Station Controller
MSC: Mobile Switching Center
BTS: Base Transceiver Station
VLR: Visitor Location Register
HLR: Home Location Register
AuC: Authentication Center
PDN : Public (Packet) Data Network
PSTN: Public Switched Telephone Network
ISDN: Integrated Services Digital Network
GMSC: Gateway Mobile Switching Center
SMSC: Short Message Service Center
SGSN :Serving GPRS Support Node
GGSN: Gateway GPRS Support Node
GPRS: General Packet Radio Service
EDGE: (Enhanced Data rates for GSM Evolution)

## Slide 56
System Architecture: Radio subsystem
  Mobile Station (MS)
    Mobile Equipment (ME)
    Subscriber Identity Module (SIM)
  Base Station Subsystem (BSS)
    Performs coding/decoding of voice
    Rate adaptation to/from the wireless network.
  Base Transceiver Station (BTS)
    Comprises antenna’s signal processing and amplifiers and Trans-receiver (TRX) units
    Connected to MS via Um interface
    Connected to BSC via Abis interface
    Range 30-100 KM (depending upon traffic)
A
BSS
Radio subsystem
Network and switching subsystem
MS
MS
Um
BTS Abis
BSC
MSC
BTS
BTS
BSC
BTS
MSC

## Slide 57
Radio subsystem
  Base Station Controller (BSC)
    Manages Radio resources for BTS
    Assigns Frequency and time slots for all MS’s in its area
    Handles call set up
    Transcoding and rate adaptation functionality
    Handover for each MS
    Radio Power control
    It communicates with MSC and BTS
NSS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
RSS
radio cell
MS MS
radio cell
MS
AUC
OSS
signaling ISDN, PSTN
PDN
O

## Slide 58
NETWORK AND SWITICHING SUBSYSTEM
    Mobile Switching Center (MSC)
    Home Location Register (HLR)
    Visitor Location Register (VLR)
NSS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
RSS
radio cell
MS MS
radio cell
MS
AUC
OSS
signaling ISDN, PSTN
PDN
O

## Slide 59
Mobile Switching Center (MSC)
Heart of the network
Manages communication between GSM and other networks
Call setup function and basic switching
Call routing
Billing information and collection
Mobility management
- Registration
- Location Updating
- Inter BSS and inter MSC call handoff
MSC does gateway function while its customer roams to other network by using HLR/VLR.
Network Switching Subsystem
NSS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
RSS
radio cell
MS MS
radio cell
MS
AUC
OSS
signaling ISDN, PSTN
PDN
O

## Slide 60
Network Switching Subsystem
Home Location Registers (HLR)
    Permanent database about mobile subscribers in a large service area (generally one per GSM network operator)
    database contains IMSI (International Mobile Subscriber Identity), MSISDN (Mobile Station International Subscriber Directory Number), prepaid/postpaid, roaming restrictions, supplementary services
Visitor Location Registers (VLR)
    Temporary database which updates whenever new MS enters its area, by HLR database
    Controls those mobiles roaming in its area
    Reduces number of queries to HLR
    Database contains IMSI,TMSI (Temporary Mobile Subscriber Identity), MSISDN, MSRN (Mobile Station Roaming Number), Location Area, authentication key

## Slide 61
OPERATION SUBSYSTEM
Operation and maintenance centre(OMC)
  Traffic monitoring
  Security management
  Accounting/billing
Authentication Center (AUC)
  Protects against intruders in air interface
  Maintains authentication keys .
  Generally associated with HLR
Equipment Identity Register (EIR)
  Database that is used to track handsets using the IMEI (International Mobile Equipment Identity)
  EIR blacklist the stolen mobile
NSS
BTS
BSC
GMSC
IWF
OMC
BTS
BSC
MSC
MSC
Abis
Um
EIR
HLR
VLR
VLR
A
BSS
RSS
radio cell
MS MS
radio cell
MS
AUC
OSS
signaling ISDN, PSTN
PDN
O

## Slide 62
GSM: cellular network
use of several carrier frequencies
not the same frequency in adjoining cells
cell sizes vary from some 100 m up to 35 km depending on user density, geography, transceiver power etc.
hexagonal shape of cells is idealized (cells overlap, shapes depend on geography)
if a mobile user changes cells
  handover of the connection to the neighbor cell

## Slide 63
GSM frequency bands
Type | Channels | Uplink [MHz] | Downlink [MHz]
GSM 850 (Americas) | 128-251 | 824-849 | 869-894
GSM 900 | 0-124, 955-1023 | 876-915 | 921-960
classical | 124 channels | 890-915 | 935-960
extended | +49 channels | 880-915 | 925-960
GSM 1800 | 512-885 | 1710-1785 | 1805-1880
GSM 1900 (Americas) | 512-810 | 1850-1910 | 1930-1990
GSM-R | 955-1024, 0-124 | 876-915 | 921-960
exclusive | 69 channels | 876-880 | 921-925

## Slide 65: 3G- Third Generation
The 3G mobile communication systems are
IMT-2000 (International Mobile Telecommunication-2000)
The standard IMT-2000 are used in ITU (International Telecommunication
Union ).
UMTS (Universal Mobile Telecommunications systems)
The standard UMTS are used in ETSI (European Telecommunication
Standard Institute).

## Slide 66
THIRD GENERATION (3G)
3G network combines aspects of the 2G network with new technologies and protocols to deliver a significantly faster data rate.
By using packet switching, the original technology was improved to allow speeds up to 14 Mbps.
It used Wide Band Wireless Network that increased clarity.
It operates at a range of 2100MHz and has a bandwidth of 15-20MHz.
Speed of up to 2 Mbps.
Increased bandwidth, capacity and data transfer rates.
Provide voice and multimedia services like high speed internet access, video, data and high quality of image transmission.
Multiple Access Techniques -- W-CDMA
3G- Third Generation

## Slide 67
UMTS Frequency band

## Slide 68
GSM vs UMTS

## Slide 69: Evolution to 3G Network
UMTS (Universal Mobile Telecommunications systems)

## Slide 70: Evolution to 3G Network
Image Credit : Qualcomm

## Slide 71: Evolution of 3G to HSPA+
Image Credit : Qualcomm

## Slide 72: 3GPP releases of 3G

## Slide 74: 3G Network and features
Digital Voice and SMS
Mobility
Mobile web browsing WCDMA : Up to 384 kbps
HSPA : Up to 7.2 Mbps
HSPA + (3.5G) up to 71.6 Mbps
Image Sharing Video Call
GPS based Services
AuC
VLR
SMSC
HLR
RNC: Radio network Controller
HLR: Home Location Register
VLR: Visitor Location Register
AuC: Authentication Center
IMS: IP Multimedia System
MSC: Mobile Switching Center
GMSC: Gateway Mobile Switching Center
SMSC: Short Message Service Center
SGSN :Serving GPRS Support Node
GGSN: Gateway GPRS Support Node
HSPA: High speed packet access

## Slide 75
4G is the fourth generation of mobile network technology, succeeding 3G and preceding 5G.
It offers significantly faster data speeds than its predecessors, with download speeds typically ranging from 10 Mbps to 100 Mbps, enabling high-definition video streaming, online gaming, and faster web browsing.
4G networks have reduced latency, improving real-time applications like video conferencing, VoIP, and gaming.
4G supports a wide range of services, including mobile broadband, voice over LTE (VoLTE), and multimedia messaging, allowing for more reliable and consistent connectivity.
Since its rollout in the late 2000s, 4G has been widely adopted across the world, providing the foundation for modern mobile communications.
4G- Fourth Generation

## Slide 76
FOURTH GENERATION (4G)
The key technologies that have made 4G possible are MIMO (Multiple Input Multiple Output) and OFDM (Orthogonal Frequency Division Multiplexing).
The most important 4G standards are WiMAX and LTE. While 4G LTE is a major improvement over 3G speeds, it is technically not 4G.
4G paved the way for the development of 5G, with many of its technologies and infrastructures being used as a base for the newer generation.
4G- Fourth Generation

## Slide 77: Key Parameters of 3G and 4G systems
Traits | 3G | 4G
Frequency Band | 1.8 – 2.5 GHz | 2- 8 GHz
Bandwidth | 5 to 20 MHz | 5 to 20 MHz
Max data rate | 2 Mb/s | 20 Mb/s (or 100 Mb/s)
Multiple access | W-CDMA, TDMA | MC-CDMA, OFDM
Switching | Circuit/packet | Packet
Coding | Convolutional, rates 1/2 & 1/3 | Concatenated codes, LDPC codes

## Slide 78: Evolution to 4G
Carrier aggregation (CA) in 4G, specifically LTE-Advanced, is a technique that combines multiple frequency bands to create a larger bandwidth channel, thereby increasing data rates and network capacity. It allows mobile devices to utilize multiple carriers simultaneously, effectively boosting throughput and improving the user experience.
Combining Carriers:
CA involves aggregating two or more component carriers (CCs), each with a bandwidth of 1.4, 3, 5, 10, 15, or 20 MHz. In LTE-Advanced, up to five CCs can be aggregated, potentially reaching a maximum bandwidth of 100 MHz.

## Slide 79: Evolution to 4G

## Slide 80: Evolution to 4G
HSS : Home Subscriber Server
HLR : Home Location Register
IMS : IP Multimedia System
PSTN: Public Switched Telephone Network

## Slide 81: 4G Network and features
Data Only Technology
Voice over LTE Mobility
SMS
Mobile Broadband High data Rate Smart Phone Mobile APPs Social Media
High Video Consumption
Uu : Radio interface between the UE & eNodeB
S1-MME: interface between the eNodeB and MME
E-UTRAN: Evolved Universal Terrestrial Radio Access Network
HSS : Home Subscriber Server
UE: User Equipment
eNodeB: base station
MME :Mobility Management Entity
PCRF: Policy and Charging Rules Function

## Slide 82: 4G Radio Capabilities
1Gbps Peak Data rate
10 bps/Hz Spectral Efficiency
10 Mbps user Experience Data rate
Upto 10 ms Latency

## Slide 83
5G is the fifth generation of cellular networks, bringing new capabilities that will create opportunities for people, businesses and society.

## Slide 84
FIFTH GENERATION (5G)
5G uses the rarely used radio millimeter bands in the 30 GHz to 300 GHz range. Testing of 5G range in mmWave has produced results approximately 500 meters from the tower.
Using small cells, carriers using millimetre wave for the deployment of 5G can improve overall coverage area. Combined with Beamforming, small cells can deliver extremely fast coverage with low latency.
Low latency is one of 5G’s most important features. 5G uses a scalable orthogonal frequency-division multiplexing (OFDM) framework.
5G benefits greatly from this and can have latency as low as one millisecond with realistic estimates to be around 1 – 10 seconds. 5G is estimated to be 60 to 120 times faster than the average 4G latency.
With speeds of up to 10 Gbps, 5G is set to be as much as 10 times faster than 4G.
Following is a brief comparison of 2G, 3G, 4G, and 5G.

## Slide 85
2G vs 3G vs 4G vs 5G
Each generation in some way has improved over its predecessor. Following is the comparison between 2G, 3G, 4G, 5G

## Slide 86: High Level 5G System
5G enables a new kind of network that is designed to connect virtually everyone and everything together including machines, objects, and devices.

## Slide 87
PDU (Protocol Data Unit) session

## Slide 88: 5G Service Based Architecture
Network can be Deployed on Virtualised / Cloud Infrastructure
User Plane
Use plane and Control plane Separation
User Plane can be located near user
Service Based Architecture
Network Functions Connect to each other on API based interface
Control Plane
Outside Connection is also on API
Disaggregated Hardware and Software
UPF : User Plane Function
DN : Data Network
PCF : Policy Control Function
AF : Application Function
UDM: Unified Data Management
NRF : Network Repository Function
NEF : Network Exposure Function
SMF : Session Management Function
AMF: Access and Mobility Management Function
AUSF : Authentication Server Function
NSSF : Network Slice Selection Function

## Slide 90: Comparison of 4G & 5G Network
PGW : Packet Data Network Gateway
SGW: Serving Gateway

## Slide 91: 5G Use cases
eMBB
uRLLC
mMTC
Public Safety
Agriculture
Health
Transport
Logistics
Education
Entertainment

## Slide 92: 5G Technologies
Channel bandwidth upto 400MHz
Freq in mm Wave
Massive MIMO
BWP
Open RAN
NFV
Network Slicing
Edge Commuting
IAB
Side Link
Satellite Integration
AI/ML
And many more
BWP : Bandwidth Part is a mechanism that allows a UE (User Equipment) to operate within a subset of the total carrier bandwidth.
NFV: Network Functions Virtualization plays a crucial role in enabling flexibility, scalability, and cost-efficiency.
IAB: Integrated Access and Backhaul is a technology that allows a single node to provide both access (connecting users) and backhaul (connecting to the core network) functions, often in a multi-hop wireless configuration.

## Slide 93: 5G Core

## Slide 94: 5G RAN - New Radio (NR)
Complete system: 5G RAN & Core

## Slide 96: 6G Usage Scenarios

## Slide 97: 6G Capabilities
9 Enhanced capabilities
6 New Capabilities

## Slide 98: 5G and EMF / Radiation

## Slide 99: Thank You